## Slide 1: Computer Architecture: Graduate Lab Report
Jiaqi Gu (jg68999)
Yuesen Lu (YL33489)

## Slide 2: Outline
Summary of RRIP
SimPoint Setup
Quantitative Evaluation
Analysis

## Slide 3: 1.1 SRRIP Cache Replacement Policy
M bits per cache block to store Re-Reference Prediction Values (RRPV) ∈[0, ]
Cache Hit: Set the block’s RRPV to 0 (Hit Policy, HP)
Cache Miss:
  No conflict
    Insert and set RRPV to (long-reference gives the best result)
  Conflicts
    Replace a block whose RRPV is
    If none, increment all RRPVs by 1 until the victim can be identified.
    If found, then insert it and set its RRPV to
A better scan-resist policy than LRU

## Slide 4: 1.2 DRRIP Cache Replacement Policy
Two Policies to dynamically choose
  Scan-resist SRRIP
  Thrash-resist Bimodal RRIP (BRRIP)
    Insert majority of cache line with RRPV of ; infrequently with RRPV of
Two Set Dueling Monitors (SDMs)
  Estimate misses for given policy on a few dedicated sets
Policy Selection Counters (PSEL)
  Determine Wining Policy
Use two SDMs for the remaining sets

## Slide 5: 2. SimPoint Setup
Cluster | Icount* | Weights
1 | 8070001932 | 0.11240
2 | 18120004274 | 0.10975
3 | 3090000819 | 0.08760
4 | 23790005563 | 0.20397
5 | 51780011854 | 0.48628
bzip2
Length of SimPoints: 30 Million
Skip first 1 million instructions
Max cluster number (K): 5
*Icount: start instruction of that trace
Cluster | Icount | Weights
1 | 278250248589 | 0.00205
2 | 2280152045099 | 0.27847
3 | 186330166230 | 0.71948
cactusADM

## Slide 6: 2. SimPoint Setup
Cluster | Icount | Weights
1 | 40980020068 | 0.58558
2 | 317520157280 | 0.24296
3 | 368940182854 | 0.02510
4 | 342870169847 | 0.14630
hmmer
Cluster | Icount | Weights
1 | 57840010926 | 0.42404
2 | 116520019948 | 0.28964
3 | 267660041304 | 0.21647
4 | 95160014702 | 0.06984
mcf

## Slide 7: 2. SimPoint Setup
Cluster | Icount | Weights
1 | 1641630399809 | 0.21044
2 | 137700030560 | 0.12626
3 | 1045680248842 | 0.19970
4 | 1038870247205 | 0.12612
5 | 2087850516085 | 0.33748
sphinx3

## Slide 8: 3.1 Quantitative Evaluation Metrics
Miss Rate
When an attempt to read or write data from the cache is unsuccessful, it results in lower level or main memory access and results in a longer latency. A better cache replacement policy should have lower miss rate.
Cycle Per Instruction, CPI
It is the average cycles per instruction in a given process. A better cache replacement policy should have lower CPI.
N: total number of traces
i: index of trace
w: weight of a trace

## Slide 9: 3.2 Methodology
Use Runspec to generate reference input and executable files of benchmarks
Use PinPoints to generate SimPoints of five benchmarks
Use Champsim_tracer file to generate tracer required by Pin tool later
Use Pin and tracer to generate trace of each SimPoint
Use Champsim to simulate based on the traces generated before

## Slide 10: 3.3 System Configuration
Configurations | Options
Branch Prediction | Bimodal
L1 Data Cache Prefetcher | No Next_Line
L2 Coherent Cache Prefetcher | No Lp_Stride
LLC Replacement Policy | LRU SRRIP DRRIP
Core | 1
LLC Set | 2048 8192
LLC Way | 8 16
LLC Cache Block (Byte) | 8

## Slide 11: 3.4 Simulation Configuration
ChampSim Simulation
  Trace Length = 30 million
  Warm-up Length = 1 million
Simulate on all traces with 48 different system configurations.

## Slide 12
3.5 Data Collection
Extract by MATLAB Script
  CPU 0 cumulative IPC
  LLC TOTAL MISS
  LLC TOTAL ACCESS

## Slide 13: Miss Rate Evaluation
Chart: DRRIP (No prefetcher)
| 256KB/16 way | 128KB/8 way | 1024KB/16 way | 512KB/8 way
bzip2 | 0.17933 | 0.37168 | 0.14499 | 0.14533
cactusADM | 0.7849 | 0.78772 | 0.627 | 0.70092
hmmer | 0.30221 | 0.45364 | 0.18463 | 0.18974
mcf | 0.5705 | 0.68586 | 0.35227 | 0.49909
sphinx3 | 0.78643 | 0.81986 | 0.15338 | 0.31145
Chart: SRRIP(No prefetcher)
| 256KB/16 way | 128KB/8 way | 1024KB/16 way | 512KB/8 way
bzip2 | 0.18467 | 0.40885 | 0.14459 | 0.14503
cactusADM | 0.76238 | 0.80224 | 0.62622 | 0.71305
hmmer | 0.29624 | 0.54816 | 0.18507 | 0.1967
mcf | 0.57799 | 0.7339 | 0.35269 | 0.5061
sphinx3 | 0.77374 | 0.83593 | 0.15478 | 0.3183
Chart: LRU(No prefetcher)
| 256KB/16 way | 128KB/8 way | 1024KB/16 way | 512KB/8 way
bzip2 | 0.17572 | 0.36911 | 0.14459 | 0.1448
cactusADM | 0.78461 | 0.78463 | 0.62569 | 0.70457
hmmer | 0.30953 | 0.45155 | 0.18507 | 0.19664
mcf | 0.60537 | 0.75265 | 0.39869 | 0.53939
sphinx3 | 0.83687 | 0.86564 | 0.16225 | 0.34719

## Slide 14: Miss Rate Evaluation
Chart: DRRIP (With prefetcher)
| 256KB/16 way | 128KB/8 way | 1024KB/16 way | 512KB/8 way
bzip2 | 0.13794 | 0.34751 | 0.10334 | 0.10366
cactusADM | 0.78571 | 0.78791 | 0.62685 | 0.70163
hmmer | 0.28771 | 0.45221 | 0.18535 | 0.19081
mcf | 0.5043 | 0.65438 | 0.28796 | 0.41597
sphinx3 | 0.79861 | 0.84657 | 0.16474 | 0.4069
Chart: SRRIP (With prefetcher)
| 256KB/16 way | 128KB/8 way | 1024KB/16 way | 512KB/8 way
bzip2 | 0.13829 | 0.37835 | 0.10311 | 0.10347
cactusADM | 0.76202 | 0.80213 | 0.62611 | 0.71296
hmmer | 0.29564 | 0.54616 | 0.1845 | 0.19607
mcf | 0.51699 | 0.67726 | 0.28746 | 0.42737
sphinx3 | 0.77653 | 0.84212 | 0.16404 | 0.36485
Chart: LRU (With prefetcher)
| 256KB/16 way | 128KB/8 way | 1024KB/16 way | 512KB/8 way
bzip2 | 0.13021 | 0.34317 | 0.10311 | 0.10327
cactusADM | 0.78436 | 0.78426 | 0.62561 | 0.7046
hmmer | 0.31 | 0.45139 | 0.1845 | 0.19596
mcf | 0.53374 | 0.69338 | 0.31787 | 0.45053
sphinx3 | 0.83979 | 0.86582 | 0.17198 | 0.40472

## Slide 15: S-Curve
Chart: Relative Performance(LRU vs DRRIP)
| bzip2 | cactusADM | hmmer | mcf | sphinx3
256KB/16 way | 0.97988 | 0.99963 | 1.0242 | 1.0611 | 1.0641
128KB/8 way | 0.99308 | 0.99608 | 0.99538 | 1.0974 | 1.0558
1024KB/16 way | 0.99721 | 0.99791 | 1.0024 | 1.1318 | 1.0579
512KB/8 way | 0.99637 | 1.0052 | 1.0364 | 1.0808 | 1.1147
Chart: Relative Performance(LRU vs SRRIP)
| bzip2 | cactusADM | hmmer | mcf | sphinx3
256KB/16 way | 0.95152 | 1.0292 | 1.0449 | 1.0474 | 1.0816
128KB/8 way | 0.90281 | 0.97805 | 0.82376 | 1.0256 | 1.0355
1024KB/16 way | 1 | 0.99916 | 1 | 1.1304 | 1.0483
512KB/8 way | 0.99842 | 0.98811 | 0.99968 | 1.0658 | 1.0907

## Slide 16: CPI Evaluation
Chart: SRRIP (No prefetcher)
| 128KB/8 way | 256KB/16 way | 512KB/8 way | 1024KB/16 way
bzip2 | 1.3186 | 1.1876 | 1.1542 | 1.1538
cactusADM | 2.3596 | 2.3297 | 2.2961 | 2.2598
hmmer | 1.0555 | 0.97927 | 0.95515 | 0.95151
mcf | 7.5499 | 6.9526 | 6.5269 | 4.79
sphinx3 | 1.763 | 1.6878 | 1.2946 | 1.1452
Chart: DRRIP (No prefetcher)
| 128KB/8 way | 256KB/16 way | 512KB/8 way | 1024KB/16 way
bzip2 | 1.3079 | 1.1817 | 1.1543 | 1.1541
cactusADM | 2.365 | 2.3563 | 2.3171 | 2.2582
hmmer | 1.0472 | 0.98347 | 0.9516 | 0.95206
mcf | 7.3592 | 6.7235 | 6.4147 | 4.7121
sphinx3 | 1.7449 | 1.7171 | 1.2891 | 1.15
Chart: LRU (No prefetcher)
| 128KB/8 way | 256KB/16 way | 512KB/8 way | 1024KB/16 way
bzip2 | 1.3104 | 1.1815 | 1.154 | 1.1538
cactusADM | 2.3656 | 2.3596 | 2.3156 | 2.2602
hmmer | 1.0491 | 0.987 | 0.95513 | 0.95151
mcf | 7.6392 | 7.066 | 6.6808 | 4.9678
sphinx3 | 1.8111 | 1.7674 | 1.3229 | 1.15

## Slide 17: CPI Evaluation
Chart: DRRIP (With prefetcher)
| 128KB/8 way | 256KB/16 way | 512KB/8 way | 1024KB/16 way
bzip2 | 1.2311 | 1.1333 | 1.1137 | 1.1135
cactusADM | 2.0788 | 2.0774 | 2.0742 | 2.0708
hmmer | 0.92706 | 0.9233 | 0.92189 | 0.92186
mcf | 5.3389 | 4.8391 | 4.5048 | 3.6873
sphinx3 | 1.1602 | 1.1399 | 1.0008 | 0.9104
Chart: SRRIP (With prefetcher)
| 128KB/8 way | 256KB/16 way | 512KB/8 way | 1024KB/16 way
bzip2 | 1.2366 | 1.1345 | 1.1136 | 1.1134
cactusADM | 2.078 | 2.0763 | 2.0737 | 2.0707
hmmer | 0.92813 | 0.92347 | 0.92196 | 0.92181
mcf | 5.4349 | 4.9998 | 4.6377 | 3.7848
sphinx3 | 1.1618 | 1.1099 | 0.97852 | 0.90774
Chart: LRU (With prefetcher)
| 128KB/8 way | 256KB/16 way | 512KB/8 way | 1024KB/16 way
bzip2 | 1.2293 | 1.1297 | 1.1135 | 1.1134
cactusADM | 2.0786 | 2.0767 | 2.0743 | 2.0709
hmmer | 0.9273 | 0.92343 | 0.92196 | 0.92181
mcf | 5.47 | 5.044 | 4.7268 | 3.8843
sphinx3 | 1.1856 | 1.1626 | 1.0012 | 0.91054

## Slide 18: S-Curve
Chart: Relative Performance(LRU vs DRRIP)
| bzip2 | cactusADM | hmmer | mcf | sphinx3
128KB/8 way | 1.0019 | 1.0002 | 1.0018 | 1.0381 | 1.038
256KB/16 way | 0.99986 | 1.0014 | 1.0036 | 1.0509 | 1.0293
512KB/8 way | 0.99973 | 0.99936 | 1.0037 | 1.0415 | 1.0262
1024KB/16 way | 0.99977 | 1.0009 | 0.99942 | 1.0543 | 1.0001
Chart: Relative Performance(LRU vs SRRIP)
| bzip2 | cactusADM | hmmer | mcf | sphinx3
128KB/8 way | 0.99379 | 1.0025 | 0.9939 | 1.0118 | 1.0273
256KB/16 way | 0.99487 | 1.0128 | 1.0079 | 1.0163 | 1.0471
512KB/8 way | 0.99982 | 1.0085 | 0.99999 | 1.0236 | 1.0219
1024KB/16 way | 1 | 1.0002 | 1 | 1.0371 | 1.0043

## Slide 19: 4.1 Analysis
Different Cache Size
  Generally larger cache size leads to smaller miss rate and smaller CPI
  The improvement caused by RRIP is not very sensitive to cache size in our experiments. Because the cache size we use is smaller than the working set of those workloads (2M), thus a better replacement policy will have better performance as it resolves capacity miss.
  Among different cache size, we can see DRRIP achieves better performance than SRRIP in CPI and miss rate under most cases.
  When cache size is small, e.g. 128KB or 256 KB, sometimes RRIP, especially SRRIP will lead to higher miss rate and higher CPI than LRU.

## Slide 20: 4.1 Analysis
Different Set Associativity
  In most cases, RRIP gains a little bit higher performance improvement in cache with 16-way set-associativity than 8-way set-associativity. But this trend may be due to different access patterns.
  DRRIP is more sensitive to set associativity than SRRIP when metric is miss rate; SRRIP is more sensitive when metric is CPI, as shown in the variation among different s-curves.

## Slide 21: 4.1 Analysis
w./w.o. Prefetcher
  In most cases, prefetcher will improvement the performance, except for sphinx3.
  CPI gets more benefit from prefetcher than miss rate.
  Without prefetcher, RRIP can achieve more performance improvement than with prefetcher.

## Slide 22: 4.2 Conclusion and Recommendation
Both DRRIP and SRRIP have slightly lower miss rate and lower CPI than LRU on most benchmarks. And DRRIP has better performance than SRRIP on most benchmarks.
In some cases, RRIP achieves worse miss rate and CPI than LRU. One possible reason is that the locality over long-interval re-reference in these benchmarks rarely happens. So the advantage of RRIP is not fully utilized.
Generally, larger cache size and more set-associativity will fully utilize the benefits from RRIP.
RRIP are recommended to be used in large LLC cache with appropriate set-associativity, while the application running on the system should have long-reference locality and scanning patterns.