## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 16
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Grad Lab

## Slide 3: Grad Lab
Compare RRIP (SRRIP and DRRIP) against LRU on a set of benchmarks
Evaluate using Simpoints of select SPEC Benchmarks on ChampSim
Simpoints and traces will be generated using Pin
Do the lab in group of 2
Submit the final presentation file (.ppt or .pdf) by Dec 10 (11:59pm)
Start early!
  Simpoint / trace generation can be time consuming!
[ Lab description ]

## Slide 4: SPEC CPU Benchmarks
Set of benchmarks announced by SPEC (Standard Performance Evaluation Corporation)
  Non-profit corporation formed to establish, maintain and endorse standardized benchmarks and tools
SPEC CPU benchmarks
  Usually divided Integer (INT) and Floating Point (FP) flavors
  Individual vs “Rate” (for multi-programmed)
  Very different characteristics per application
History
  SPEC CPU 92, 95, 2000, 2006, and 2017
We will use a subset of 2006 benchmarks
  bzip2, cactusADM, hmmer, mcf, sphinx3 (used in RRIP paper)

## Slide 5: SimPoints
Motivation
  Simulating full program is often too time consuming
  Programs typically exhibit phase behavior
  How do we characterize and identify these phases automatically?
Methodology
  Collect Basic Block Vector (BBV) for each interval
    BBV: Histogram of how many times each basic block was executed in interval
  Reduce dimension of BBV to 15 using random linear projection
  Use K-means clustering: Partition data into k clusters
  Choose clustering with smallest k, such that BIC score is at least 90% of the best score
    BIC (Bayesian Information Criterion): Goodness of fit
[ https://cseweb.ucsd.edu/~calder/papers/ASPLOS-02-SimPoint.pdf ]

## Slide 6: Example Phase Behavior identified by SimPoints
gcc-166

## Slide 7: Weighting Stats with SimPoints
Stats of full run can be projected by weighting stats from individual SimPoints
E.g., 3 SimPoints with weights [.22, .33, .45] and CPIs of (CPI1, CPI2, CPI3):
  CPI = 0.22 * CPI1 + 0.33 * CPI2 + 0.45 * CPI3
Watch out when weighting them:
  Raw counts can be weighted:
    # of cycles, cache misses, cache accesses, …
  But not all “rate” stats can be weighted:
    IPC, cache miss rates, branch misprediction rate, …
    Weight the individual components first and then calculate rate!
  “per-instruction” stats can be safely weighted:
    CPI, cache MPKI (miss-per-kilo-instructions), branch MPKI, …

## Slide 8: Pin: Dynamic Binary Instrumentation
Goals:
  Provide easy-to-use, portable, transparent, and efficient instrumentation
Much faster than simulation
  Heavily depends on type of analysis
  Intended for light-weight analysis
Uses “dynamic compilation” (also called just-in-time compilation) to instrument executables while they are running
Uses several optimizations to make it fast
We will use it to generate BBVs and traces for our simulator
[ http://www.ckluk.org/ck/papers/pin_pldi05.pdf ]

## Slide 9: Simulators
Several architecture simulators exist
  Different features and trade-offs
  gem5: http://gem5.org
  Sniper: http://snipersim.org
  ZSim: https://github.com/s5z/zsim
  ChampSim: https://github.com/ChampSim/ChampSim
ChampSim
  Trace-based (faster than execution-driven, but less accurate)
  This simulator was used for the 2nd Cache Replacement Championship ( https://crc2.ece.tamu.edu )
  Trace generated through PinTools
  We will use it mainly for its ease-of-use and speed (to help with your experiments)

## Slide 10: RRIP: Re-reference Interval Prediction
A form of cache replacement policies that focus on cases that perform badly under LRU (Least Recent Used)
We will discuss in greater detail during the cache lectures
[ http://www.jaleels.org/ajaleel/publications/isca2010-rrip.pdf ]

## Slide 11: Grad Lab (Reprise)
Compare RRIP (SRRIP and DRRIP) against LRU on a set of benchmarks
Evaluate using Simpoints of select SPEC Benchmarks on ChampSim
Simpoints and traces will be generated using Pin
Do the lab in group of 2
Submit the final presentation file (.ppt or .pdf) by Dec 10 (11:59pm)
Start early!
  Simpoint / trace generation can be time consuming!
[ Lab description ]

## Slide 12: What to submit?
Slides should include the following information:
  Brief summary of the RRIP cache replacement policies
  Your SimPoint setup
    # of SimPoints, length of SimPoints used
    List of identified SimPoints and weights for each benchmark
  Quantitative evaluation
    Important metrics for comparing cache replacement policies & rationale
    Methodology (system configurations, how you collected data)
    Your evaluation data for RRIP vs. LRU
      Different cache sizes
      Different set-associativities
      S-curve (refer to Figure 9 in the RRIP paper)
      Effect of prefetch vs. no prefetch
  Analysis
    Discuss your observations, insights from the data
    Conclude and make recommendation

## Slide 13: Last time
Interrupts and Exceptions
Caches

## Slide 14: One Possible Direct-Mapped Cache Implementation
a
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
a
00
01
10
11
Cache
SRAM
2
addr_tag + valid + data
Mem
(DRAM)
4
data
Cache state is RAM!
Implement cache as a single SRAM
Need appropriate comparators
Memory is implemented as a DRAM

## Slide 15: Conflicts
What if our access pattern is mostly contiguous but not completely?
For (I = 0; I < 3; ++I) {
  A += mem[i];
}
A += mem[5];
Assume mem == 0b1000
ldw Ra, 0b1000
ldw Rt, 0b1001; add Ra , Ra , Rt
ldw Rt, 0b1010; add Ra , Ra , Rt
ldw Rt, 0b1101; add Ra , Ra , Rt
…….
ldw Rb, 0b1001; cache hit?
a
a
b
c
d
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
addr
Addr[1:0]
00
01
10
11
b
10
a
c
b
d
10
10
10
11

## Slide 16: Sets
Each cacheable memory location is mapped to a set of cache locations
A set is one or more cache locations
Generally (but not always) set size is a power of 2
Total number of cache-lines is divisible by number of sets
  Otherwise, waste some cache-lines
Thus, for this example, expect set sizes of 1, 2, 4
Direct mapped is set size == 1!
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
00
01
10
11

## Slide 17: Sets
Each cacheable memory location is mapped to a set of cache locations
A set is one or more cache locations
Generally (but not always) set size is a power of 2
Total number of cache-lines is divisible by number of sets
  Otherwise, waste some cache-lines
Thus, for this example, expect set sizes of 1, 2, 4
Direct mapped is set size == 1!
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
00
01
10
11

## Slide 18: 2-Way Set-Associative
Each set is 2 entries big
Which addr bits select set?
Either entry can store any cache-line that maps to that set
For (I = 0; I < 3; ++I) {
  A += mem[i];
}
A += mem[5];
Assume mem == 0b1000
ldw Ra, 0b1000
ldw Rt, 0b1001; add Ra , Ra , Rt
ldw Rt, 0b1010; add Ra , Ra , Rt
ldw Rt, 0b1101; add Ra , Ra , Rt
ldw Rb, 0b1001; cache hit?
Set 1
Set 0
0
1
1000
1001
1010
1101

## Slide 19: Can Same Structure Implement a 2-Way Set-Associative Cache?
a
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
a
00
01
10
11
Cache
SRAM
2
addr_tag + valid + data
Mem
(DRAM)
4
data
Finding the right tag?

## Slide 20: One Possible 2-Way Set-Associative Cache Implementation
Cache is simply RAM
Implement 2-way set-associative cache as a two SRAMs
Similar to Banked Memory
  But use same address for both
  Double bandwidth
Cache
0
1
Cache
SRAM
addr_tag + v + data
0
1
Cache
SRAM
addr_tag + v + data

## Slide 21: 4-Way Set-Associative (Fully Associative for a 4-entry cache)
Each Set 4 entries big
Every entry can store any cache-line that maps to that set
ldw Ra, 0b0000
ldw Rt, 0b0100
ldw Rt, 0b1000
ldw Rt, 0b1100
ldw Rb, 0b0100; cache hit?
Tags?
0
0000
1000
0100
1100

## Slide 22: Set-Associative vs. Direct Mapped
What are the tradeoffs?
Set-Associative Pros
  Generally higher hit rate
  Better utilization of cache resources
Direct-Mapped Pros
  Simpler
  Faster

## Slide 23: Locality again
So far: temporal locality
What about spatial?

## Slide 24: Example: Block Size (Cache-Line Size) of 2 (Direct Mapped Cache)
ldb Ra, 1000
ldb Rb, 1001
ldb Rc, 1010
ldb Rd, 1011
a
a
b
c
d
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
addr
Addr[2:1]
00
01
10
11
a:b
c:d
=
Hit?
[3]
What is total cache size?
Which addr bits used?

## Slide 25: What about writes?
What does STB do?
Options:
  If miss, just write directly to memory?
    Write no allocate – don’t bother caching
    Write allocate – first fill cache from memory and now it’s a hit
  If hit, just write to cache?
    Writeback cache – write when evicting (needs “dirty” bit)
    Writethrough cache – write to both cache and memory
Depends on what you think happens more often
  Access soon after a write – write allocate
  Multiple stores to same line – write back

## Slide 26: Cache Naming and Placement
Cache namespace is the same as the memory namespace
Cache placement will be as below for:
  b bits in a memory address
  2n-way set-associative cache
  S sets (s = log2S)
  L bytes of data in a cache line (l = log2L)
  Cache size?
    Data?
    Tag?
tag
index
offset
0
l
l+s
b-1

## Slide 27: A better diagram?
LC3b architecture with 512B memory and a cache:
  64B capacity, 4B cache blocks (cache lines), 2-way associative
Set 1
Set 0
abcd
efgh
ijkl
mnop
1000
1001
1110
1101
Set 3
Set 2
qrst
uvwx
yzAB
CDEF
1100
1001
1010
1111
Set 5
Set 4
GHIJ
KLMN
OPQR
STUV
1111
1101
1000
1001
Set 7
Set 6
WXYZ
0123
4567
89#$
1010
1001
1000
1101
tag
index
offset
0
1
4
8
100010001 = ?
110111111 = ?
111000000 = ?
110100110 = ?

## Slide 28: A better diagram?
LC3b architecture with 512B memory and a cache:
  64B capacity, 4B cache blocks (cache lines), 2-way associative
Set 1
Set 0
abcd
efgh
ijkl
mnop
1000
1001
1110
1101
Set 3
Set 2
qrst
uvwx
yzAB
CDEF
1100
1001
1010
1111
Set 5
Set 4
GHIJ
KLMN
OPQR
STUV
1111
1101
1000
1001
Set 7
Set 6
WXYZ
0123
4567
89#$
1010
1001
1000
1101
tag
index
offset
0
1
4
8
100010001 = L (M)
110111111 = $ (8)
111000000 = e (h)
110100110 = o (n)

## Slide 29: A better diagram?
LC3b architecture with 512B memory and a cache:
  64B capacity, 4B cache blocks (cache lines), 2-way associative
abcd
efgh
ijkl
mnop
1000
1001
1110
1101
qrst
uvwx
yzAB
CDEF
1100
1001
1010
1111
GHIJ
KLMN
OPQR
STUV
1111
1101
1000
1001
WXYZ
0123
4567
89#$
1010
1001
1000
1101
tag
index
offset
0
1
4
8
1000
1001
1100
1001
1111
1101
1010
1001
1110
1101
1010
1111
1000
1001
1000
1101
efgh
mnop
uvwx
CDEF
KLMN
STUV
0123
89#$
abcd
ijkl
qrst
yzAB
GHIJ
OPQR
WXYZ
4567
Or
Tag array
Data array

## Slide 30: Terms: Types of Misses
Compulsory
  First access
Conflict
  Cache is not associative enough
Capacity
  Cache is not big enough, forced to make room
How to determine miss type:
  Compulsory
    no choice (first time seen or coherence invalidation)
  Capacity
    Simulate fully-associate cache with capacity, line size, and alloc/replacement policy; is miss – capacity miss
  Conflict
    Simulate given cache, if miss but not capacity miss, then conflict
30
Notes: 30

## Slide 31: What To Do On Miss?
Put into cache or not?
  Any reason not to put into cache?
Difference between loads and stores?
31
Notes: 31

## Slide 32: Replacement Policy
Which block should be replaced?
  Direct mapped?
  Associative caches?
Replacement Policy
  least-recently-used (LRU)
    difficult to implement perfect LRU
  Random
  FIFO (uncommon)
  LIFO (uncommon)
  Optimal?
    Belady’s algorithm: Replace most distant reuse in the future
32
Notes: 32

## Slide 33: One Implementation of Hardware LRU
33
0 1 2 3
3 0 0 0 0
2 0 0 0 0
1 0 0 0 0
0 0 1 1 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 33

## Slide 34: One Implementation of Hardware LRU
34
0 1 2 3
3 0 0 0 0
2 0 0 0 0
1 1 0 1 1
0 0 0 1 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 34

## Slide 35: One Implementation of Hardware LRU
35
0 1 2 3
3 0 0 0 0
2 1 1 0 1
1 1 0 0 1
0 0 0 0 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 35

## Slide 36: One Implementation of Hardware LRU
36
0 1 2 3
3 1 1 1 0
2 1 1 0 0
1 1 0 0 0
0 0 0 0 0
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 36

## Slide 37: One Implementation of Hardware LRU
37
0 1 2 3
3 0 1 1 0
2 0 1 0 0
1 0 0 0 0
0 0 1 1 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 37

## Slide 38: One Implementation of Hardware LRU
38
0 1 2 3
3 0 1 0 0
2 1 1 0 1
1 0 0 0 0
0 0 1 0 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 38

## Slide 39: One Implementation of Hardware LRU
39
0 1 2 3
3 0 1 0 0
2 1 1 0 1
1 0 0 0 0
0 0 1 0 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Row with lowest binary value is LRU!
Notes: 39

## Slide 40: Tree-based Pseudo-LRU
0
0
0
1
1
0
A
0
1
1
A
B
1
0
1
A
C
B
0
0
0
A
C
B
D
1
1
0
E
C
B
D

## Slide 41: General Rule: Bigger == Slower
How big should the cache be?
  Too small and too much memory traffic
  Too large and cache slows down execution (high latency)
Make multiple levels of cache
  Small L1 backed up by larger L2
  Today’s processors typically have 3 cache levels
41
CPU
Cache
$
Memory
Cache
$
Level 1
(L1 $)
Level 2 (L2 $)
Notes: 41

## Slide 42: How much does a cache hierarchy help?
n load instructions
Total time T: Add up fraction of instructions at particular level multiplied by access latency at that level
T = ( h1*1 + (1-h1)*h2*(1+10) + (1-h1)*(1-h2)*(1+10+100) ) * n
  h1: hit rate at L1$
  h2: hit rate at L2$
CPU
Cache
$
Memory
100 cycles
Cache
$
L1 $
1 cycle
L2 $
10 cycle

## Slide 43: Terms: Types of Misses
Compulsory
  First access
Conflict
  Cache is not associative enough
Capacity
  Cache is not big enough, forced to make room
How to determine miss type:
  Compulsory
    no choice (first time seen or coherence invalidation)
  Capacity
    Simulate fully-associate cache with capacity, line size, and alloc/replacement policy; is miss – capacity miss
  Conflict
    Simulate given cache, if miss but not capacity miss, then conflict
43
Notes: 43

## Slide 44: Other cache optimizations
Latency
  Anything other than levels?
Hit rate
  Reduce misses
Conflict misses
  Associativity tradeoffs
  Victim cache
Compulsory misses
  Cache line size
  Prefetch
Capacity misses
  Replacement policies

## Slide 45: Critical Word First
Memory bus is generally one or two words wide
  Pentium 4 is 64b wide, 32b words
Cache-line fills require multiple words over bus
A simple cache-fill would always start on word 0
If you have an 8 word cache-line, and you miss on the 5th word, with a 1 word bus, you need to wait for the 5th word
  Why not start on the 5th word?
Design logic to do so

## Slide 46: Caches can be specialized for data and instructions
Memory is read for every instruction
  Lots of spatial locality
    instructions tend to follow one another
  Lots of temporal locality
    Programs have loops
    Programs are often not that big
Can have a special cache just for instructions
  Reduce conflicts with data
  Perhaps longer cache lines
  Can have very high hit rate if data doesn’t evict instructions
All processors today (almost) have separate ICache and DCache

## Slide 47: Cut down on tag lookup?
Predict where the data is
E.g., way prediction

## Slide 48: Prefetching
Issue loads that will miss early
Done by
  User (prefetch instructions)
  Compiler (prefetch instructions)
  Hardware (look for patterns)

## Slide 49: Victim Caches (Jouppi)
Associative caches expensive
Sometimes associativity necessary to get reasonable hit rate
  Some memory access patterns need associativity
  But perhaps on a small number
Combine a large direct-mapped cache with a small fully-associative cache
  Fill fully-associative with conflicts from direct-mapped cache

## Slide 50: Cache Control Instructions
Enable control over placement and replacement
PowerPC example:
  dcbt: data cache block touch
  dcbtst: data cache block touch for store
  dcbz: data cache block zero
  dcbst: data cache block store
    Stores dirty data back to memory
  dcbf: data cache block flush

## Slide 51: Placement/replacement optimizations
Dead block prediction
LRU-stack location
Blend LRU and LFU
Inter-reference intervals
…

## Slide 52: RRIP

## Slide 53: Does SW care about cache (is it microarch)?
Recall: If architectural state changes are unaffected  uarch
So, despite cache control instructions and prefetch a cache (for now) is uarch
  We’ll revisit when we talk about parallelism

## Slide 54: Caches and Virtual Memory

## Slide 55: What did we learn? Caches: Automatic Management of Fast Storage
Assumptions:
  memory access (~100ns) >> cache access (~1ns)
    Cache is smaller, faster, more expensive than memory
  Programs exhibit temporal locality
    If an item is referenced, it will tend to be referenced again soon
  Programs exhibit spatial locality
    If an item is referenced, the next item in memory is likely to be accessed soon
55
CPU
Cache
$
Memory
Notes: 55